## Slide 1
Logical & Shift Instructions
in ARM Cortex-M3
AND, ORR, EOR, BIC, ORN (3.5.2) + ASR, LSL, LSR, ROR, RRX (3.5.3)
TEAM 11 | Microcontroller Course | Ref: ST PM0056 Rev 7, pages 75-76
Rasel Ahammed - 2310776141
Md. Shoriful Islam - 2310376113
Mahamudul Hasan Masum - 2310876111
Notes: Introduce Team 11 and the topic: two groups of ARM Cortex-M3 instructions. Logical ones calculate bit by bit; shift ones move bits left or right.

## Slide 2
What We Will Cover
1 Logical instructions: AND, ORR, EOR, BIC, ORN
2 Shift & rotate: ASR, LSL, LSR, ROR, RRX
3 Flags & restrictions: N, Z, C, V
4 Worked examples in binary
5 Real use (bit set / clear / toggle) + summary
Flags: N = Negative, Z = Zero, C = Carry, V = Overflow
Notes: Five parts: logical, shift/rotate, flags, worked examples, real use. Flags are tiny status bits showing how the last result looked.

## Slide 3
Basics You Need First
Register
A tiny 32-bit storage box inside the CPU
R0-R12 are general purpose; SP and PC are special
Bit 31 = leftmost bit, bit 0 = rightmost bit
Hex shortcut: 1 hex digit = 4 bits
Hex | Binary
0x0 | 0000
0x5 | 0101
0xA | 1010
0xF | 1111
Flags
Status bits kept by the CPU: N, Z, C, V
Updated only when the S suffix is used
Later used by conditions like EQ / NE
Operand2
The flexible second input
Can be a register, a constant (#imm) or a shifted register
Example: ORN R7,R11,R14,ROR #4
Easy point: 0xFF = 1111 1111 (8 ones). 0xF0 = 1111 0000. 0x0F = 0000 1111.
Notes: Explain registers (32-bit boxes), hex (1 digit = 4 bits) and flags before the instructions. This makes everything after it easy to follow.

## Slide 4
3.5.2 Logical Instructions
Bitwise: each bit of Rn is combined with the same bit of Operand2
op{S}{cond} {Rd,} Rn, Operand2
Syntax parts
op: AND, ORR, EOR, BIC, ORN
S: update flags (optional)
cond: condition, e.g. EQ (optional)
Rd: destination register
Rn: first operand
Operand2: register, #imm or shifted register
Operations
AND: bitwise AND (mask)
ORR: bitwise OR (set bits)
EOR: exclusive OR (toggle)
BIC: Rn AND NOT Operand2 (clear bits)
ORN: Rn OR NOT Operand2
Notes: Bitwise means bit 0 of Rn meets bit 0 of Operand2, bit 1 meets bit 1, and so on. S and cond are optional extras.

## Slide 5
AND, ORR, EOR
A | B | AND | ORR | EOR
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 0
AND: both must be 1 (mask / keep bits)
ORR: either is 1 (set bits)
EOR: different gives 1 (toggle bits)
Result goes to Rd; Rn and Operand2 unchanged
AND R0,R1,#0x0F ; keep low 4 bits
1011 0110
0000 1111
0000 0110
ORR R0,R1,#0x0F ; set low 4 bits
1010 0101 | 0000 1111
1010 1111
EOR R0,R1,#0x0F ; toggle low 4 bits
1010 0101 ^ 0000 1111
1010 1010
Rule: where Operand2 has a 1, that bit is affected.
Notes: Truth table: AND needs both 1, ORR needs any 1, EOR needs different bits. Walk through the three binary examples on the right.

## Slide 6
BIC and ORN
Both use the complement (NOT) of Operand2
BIC (Bit Clear)
Rd = Rn AND (NOT Operand2)
Operand2 bit = 1 gives result bit = 0
Think: "1 means clear this bit"
BIC R0,R1,#0xAB
R1 = 1111 1111
0xAB = 1010 1011
NOT 0xAB = 0101 0100
R0 = 0101 0100 (0x54)
ORN (OR NOT)
Rd = Rn OR (NOT Operand2)
Operand2 bit = 0 gives result bit = 1
On 32 bits the upper bits become 1
ORN R7,R11,#0xF0
R11 = 0000 1111
0xF0 = 1111 0000
NOT 0xF0 = 0000 1111
R7 = 0xFFFFFF0F (32-bit)
Notes: BIC and ORN flip Operand2 first. BIC: a 1 in Operand2 clears that bit. ORN: 0 in Operand2 becomes 1. On 32 bits NOT also sets the upper bits.

## Slide 7
Logical Ops: Flags & Restrictions
If S is specified
N and Z updated from the result
C may update while computing Operand2
V is not affected
Restrictions
Do not use SP or PC as registers
Condition suffix EQ runs only if Z = 1
AND R9, R2, #0xFF00
ORREQ R2, R0, R5
ANDS R9, R8, #0x19
EORS R7, R11, #0x18181818
BIC R0, R1, #0xAB
ORN R7, R11, R14, ROR #4
ORNS R7, R11, R14, ASR #32
Notes: With S, N and Z come from the result, C may change, V never changes. SP and PC are not allowed. EQ runs the instruction only when Z = 1.

## Slide 8
Worked Example: Logical Math
Binary view, 8 bits for clarity
Instruction | Rn | Operand2 | Result
ANDS R9,R8,#0x19 | 0010 1101 | 0001 1001 | 0000 1001
ORR R0,R1,R2 | 1100 0011 | 0000 1111 | 1100 1111
EORS R7,R11,#0xFF | 1010 1010 | 1111 1111 | 0101 0101
Check
ANDS: 0x09 is non-zero, so Z = 0; top bit 0, so N = 0
EOR with all 1s = NOT (flips every bit)
BIC with 0xAB clears bits 0, 1, 3, 5, 7
Notes: Go row by row in binary. ANDS gives 0000 1001, not zero, so Z = 0. EOR with all 1s flips every bit, like NOT.

## Slide 9
3.5.3 Shift & Rotate Instructions
ASR: arithmetic shift right | LSL/LSR: logical shift | ROR: rotate right | RRX: rotate right extend
op{S}{cond} Rd, Rm, Rs
op{S}{cond} Rd, Rm, #n
RRX{S}{cond} Rd, Rm
Shift length n
ASR, LSR: 1 to 32
LSL: 0 to 31
ROR: 1 to 31
Operands & notes
Rd: destination
Rm: value to shift (unchanged)
Rs: shift register, lowest byte used
n: constant shift length
RRX shifts by exactly 1
MOV Rd,Rm is preferred over LSL Rd,Rm,#0
Notes: Three forms: shift by register, by constant, and RRX which always shifts by 1. Rm is never changed; the answer goes to Rd.

## Slide 10
LSL and LSR
Logical shifts: empty bits are filled with 0
LSL: shift left
0 enters on the right
Shift by n = multiply by 2^n
C = last bit shifted out
LSLS R1,R2,#3 ; R2 = 11
0000 1011 (11)
0001 0110 (22)
0010 1100 (44)
0101 1000 (88) = R1
11 x 2^3 = 88
LSR: shift right
0 enters on the left
Shift by n = unsigned divide by 2^n
C = last bit shifted out
LSR R4,R5,#2 ; R5 = 180
1011 0100 (180)
0101 1010 (90)
0010 1101 (45) = R4
180 / 2^2 = 45
Notes: LSL doubles per step: 11 becomes 88 after 3 steps. LSR halves per step: 180 becomes 45 after 2 steps. Zeros fill the empty side.

## Slide 11
ASR (Arithmetic Shift Right)
The sign bit is copied in, so signed numbers keep their sign
Bits move right by n; top (sign) bit is replicated
Signed divide by 2^n (rounds toward minus infinity)
Positive numbers: same as LSR
Negative numbers stay negative
ASR R7,R8,#2 ; R8 = -16
1111 0000 (-16)
1111 1000 (-8)
1111 1100 (-4) = R7
LSR would give:
0011 1100 (60) WRONG
32-bit: R8 = 0xFFFFF000 (-4096) ASR R7,R8,#9 R7 = 0xFFFFFFF8 (-8) (LSR gives 0x007FFFF8, wrong for signed)
Signed: use ASR. Unsigned: use LSR.
Notes: ASR copies the sign bit, so -16 becomes -8 then -4. LSR would put zeros in and give a wrong positive 60. Signed: ASR.

## Slide 12
ROR and RRX
Rotate: bits that leave one side re-enter the other
ROR (Rotate Right)
Bit shifted out of bit 0 enters bit 31
No bit is lost; n = 1 to 31 (or Rs)
ROR R4,R5,#1
0000 0011
1000 0001 = R4
ROR R4,R5,#4
1010 0101
0101 1010 = R4
RRX (Rotate Right Extend)
Shifts right by 1 through the C flag
Old C goes to bit 31; bit 0 goes to C
RRX R4,R5 ; C = 1
R5 = 0000 0010
R4 = 1000 0001
New C = 0 (with S suffix)
32-bit: 0x00000002
-> 0x80000001
Notes: ROR is a loop: the bit leaving bit 0 enters bit 31. RRX is a loop of 33 bits because the C flag joins in.

## Slide 13
Shift Instructions: Flags & Restrictions
If S is specified
N and Z updated from the result
C = last bit shifted out
Exception: shift length 0, C unchanged
Restriction
Do not use SP or PC
ASR R7, R8, #9
LSLS R1, R2, #3 ; updates flags
LSR R4, R5, #6
ROR R4, R5, R6 ; by low byte of R6
RRX R4, R5
Notes: Shift flags: N and Z from the result, C is the last bit that fell out. If shift length is 0, C stays unchanged.

## Slide 14
Flags Explained with Examples
Flag | Meaning | Example
N | Bit 31 of result is 1 (negative) | Result 0x80000000 gives N = 1
Z | Result is exactly 0 | ANDS with no common 1s gives Z = 1
C | Last bit shifted out | LSLS 1000 0001 by #1 gives C = 1
V | Signed overflow | Not changed by logical or shift ops
ANDS R0,R1,R2
R1 = 1010 0000
R2 = 0000 1111
R0 = 0000 0000
-> Z = 1, N = 0
LSLS R0,R1,#1
R1 = 1000 0001
R0 = 0000 0010
last bit out was 1
-> C = 1, Z = 0
Easy point: S = "show the result in the flags". Without S, flags stay unchanged.
Notes: Show the four flags with a mini example each. Stress: without the S suffix nothing changes in the flags.

## Slide 15
Easy Memory Tricks
Instruction | How to remember it
AND | Both must say YES (1 and 1 gives 1). Used to mask
ORR | Any ONE yes is enough. Used to set bits
EOR | Spot the difference: different gives 1. Used to toggle
BIC | Bit Clear: a 1 in Operand2 erases that bit
ORN | OR, but Operand2 is flipped first
LSL | Move left: each step doubles the number
LSR | Move right: each step halves it (unsigned)
ASR | Like LSR but copies the sign bit (signed)
ROR | Carousel: bit leaving the right re-enters on the left
RRX | Carousel with one extra seat: the C flag
Notes: Read the memory tricks aloud. These one-liners are what the audience will remember.

## Slide 16
Quick Comparison
Instruction | Effect | Math view
AND | keep / mask bits | A & B
ORR | set bits | A ¦ B
EOR | toggle bits | A ^ B
BIC | clear bits | A & ~B
ORN | OR with NOT | A ¦ ~B
LSL / LSR | shift, fill 0 | x 2^n / unsigned / 2^n
ASR | shift, keep sign | signed / 2^n
ROR / RRX | rotate | no bits lost
Notes: Summary table. If asked the difference between LSR and ASR: zero fill versus sign fill.

## Slide 17
Real Use: Controlling Bits (GPIO)
; R0 = port register value
ORR R0,R0,#0x20 ; set bit 5 0000 0000 -> 0010 0000
BIC R0,R0,#0x20 ; clear bit 5 0010 0000 -> 0000 0000
EOR R0,R0,#0x20 ; toggle bit 5 0000 0000 -> 0010 0000
ANDS R1,R0,#0x20 ; test bit 5
BEQ off ; Z=1 means bit is 0
LSL R1,R2,#2 ; R2 x 4 (5 -> 20)
LSR R3,R2,#1 ; R2 / 2 (20 -> 10)
Why it matters
Control pins, flags, timers
Pack / unpack data fields
Fast multiply / divide by powers of 2
Needs no extra memory
Task | Use
Set bit | ORR
Clear bit | BIC
Toggle bit | EOR
Test bit | ANDS
Notes: Real embedded use: ORR turns a pin on, BIC off, EOR toggles it, ANDS tests it. LSL and LSR are fast multiply and divide by 2.

## Slide 18
Which Instruction Should I Use?
I want to... | Use | Example
Keep only some bits | AND | AND R0,R1,#0x0F
Force bits to 1 | ORR | ORR R0,R0,#0x20
Force bits to 0 | BIC | BIC R0,R0,#0x20
Flip bits | EOR | EOR R0,R0,#0x20
Test a bit | ANDS + BEQ | ANDS R1,R0,#0x20
Multiply by 2^n | LSL | LSL R1,R2,#2
Divide unsigned by 2^n | LSR | LSR R3,R2,#1
Divide signed by 2^n | ASR | ASR R7,R8,#9
Rotate / swap nibbles | ROR | ROR R4,R5,#4
Shift through carry | RRX | RRX R4,R5
Notes: Use this table as a cheat sheet: pick the instruction from what you want to do.

## Slide 19
Common Mistakes & Fixes
Mistake | Fix
Using LSR on negative signed numbers | Use ASR to keep the sign
Expecting flags without the S suffix | Write ANDS, LSLS, EORS...
Mixing up BIC and AND | In BIC, a 1 in Operand2 CLEARS that bit
Forgetting NOT works on all 32 bits | ORN / BIC give 0xFFFFFF0F style results
Using SP or PC as a register | Use R0-R12 instead
Shift length out of range | LSL 0-31, ROR 1-31, ASR/LSR 1-32
Notes: Cover the typical mistakes so the audience avoids them: LSR on signed numbers, missing S, BIC vs AND.

## Slide 20
Summary
Logical ops work bit by bit: AND, ORR, EOR, BIC, ORN
Shifts move bits: LSL, LSR, ASR; rotates: ROR, RRX
S suffix updates N, Z (and C for shifts)
Never use SP or PC with these instructions
Thank You | Team 11
Notes: Four key points to repeat. Say thank you and ask for questions.